## Slide 1: Introduction to Internal Dosimetry
Richard Bull

## Slide 2: Internal dosimetry
Source is internal within body, due to
  Ingestion
  Injection (wound)
  Absorption
  Inhalation
Person is committed to receive a dose for as long as material is within body
Cannot be measured directly

## Slide 3: Internal Dosimetry
Need to calculate the dose from internally-deposited radionuclides
Direct methods are impossible, so we must use indirect methods
External dose rate ends when the worker is removed from the radiation
field
Internal dose rate continues when the worker is removed from the source of contamination
External dose is dominated by low LET radiation, internal dose usually high LET

## Slide 4: Methods of Internal Dosimetry
  Three detection strategies:
Measure activity before it enters the body—air sampling
Measure activity when it is in the body---in-vivo monitoring, autopsy
Measure activity as it leaves the body---excretion sampling

## Slide 5: Air monitoring

## Slide 6: In-vivo monitoring

## Slide 7: In-vitro monitoring (bioassay)
Urine sampling
  Indicates activity in circulation within body
Faecal sampling
  Indicates activity within the gut and lung
Dependent on solubility of inhaled material
Sensitivity | Soluble 241 Am | Insoluble 241 Am
Annual urine | 0.5 mSv | 4 mSv
Annual faecal | 3 mSv | 0.5 mSv

## Slide 8: Interpretation
We need to relate excretion/retention to intake
Need to relate intake to dose
Require biokinetic models (lung, systemic organs etc)
Require dosimetric models (radiation transport between source organs and target organs)

## Slide 9: Internal dosimetry modelling & assessment
Overview of biokinetic processes

## Slide 10: Uncertainties
Point estimates of intake and organ dose are relatively straightforward
However there are large uncertainties in measured quantities and model parameter values
Assign prior probability distributions to these quantities
Use a Bayesian method (WELMOS, Markov Chain MC) to produce posterior distributions of intake and dose
Provide the epidemiologists with calendar year organ doses and uncertainties.
!